## Slide 1
046882 HW/SW Co-design · Final project
Faster Python: nbody & raytrace
Profiling, software optimization and a hardware accelerator for pyperformance benchmarks
Student 1: Yousef Atrash · Student 2: Housin Mohammed Agbaria
1.60x
nbody, software optimization identical results
2.10x
raytrace, software optimization identical image
5.7x
nbody, hardware accelerator (estimate, incl. PCIe overhead)
Draft: this presentation is not final and will be finalized before the presentation day.
Notes: Introduce the project: two pyperformance benchmarks, nbody (a physics simulation) and raytrace (a small ray tracer). We profiled both, optimized them in Python, and designed a hardware accelerator for nbody. The three numbers are the headline results; every one of them is backed by measurements we will show.

## Slide 2
How we worked
The talk follows the same order as the project
1
Understand
read the code, data structures
2
Measure
pyperformance baseline
3
Profile
perf, flame graphs, py-spy, counters
4
Optimize
one change at a time, measure each
5
Verify
output must stay bit-identical
6
Accelerate
Verilog accelerator for nbody
Rule we kept throughout: every change is its own variant, measured on its own with pyperformance --rigorous, and checked to give exactly the same output as the original.
Notes: This is the structure of the talk and of our work. Profiling (3) drives the optimizations (4), and every optimization is verified (5) before we trust its number. The accelerator (6) is designed for the part that software cannot fix.

## Slide 3
1
Measuring on a noisy single-CPU VM
If the noise is bigger than the effect, the result means nothing
Environment: course QEMU image, Ubuntu 22.04, 1 vCPU, Python 3.10.12, pyperformance 1.14.0
Timing: pyperformance run --rigorous: 20 processes x 3 values = 120 samples per benchmark
Stability: pyperf system tune (CPU pinning, IRQs moved away) before every timing session
Statistics: median and MAD (robust to outliers), mean and std, histograms
Correctness: verify scripts compare every result bit for bit with the original
raytrace baseline spread
±84 ms
first default run (±10%, bigger than the 7% target)
±19 ms
tuned + rigorous (±2%, 120 samples)
The long tail of slow runs came from the VM being interrupted, not from the benchmark: the median barely moved (816 -> 809 ms), the tail disappeared.
Notes: Before optimizing anything we made sure we could trust our numbers. The first raytrace run had a spread of plus-minus 10 percent, larger than the 7 percent improvement the project asks for. Tuning the VM and taking 120 samples brought it to 2 percent. We report medians because a few interrupted runs pull the mean up.

## Slide 4
2
nbody: planets under gravity
Sun + 4 giant planets, 20000 time steps per benchmark iteration
Sun
Jupiter
Saturn
Uranus
Neptune
10 pairs per step · O(N²) pair loop
def advance(dt, n, bodies, pairs):
for i in range(n):
for (([x1,y1,z1], v1, m1),
([x2,y2,z2], v2, m2)) in pairs:
dx = x1-x2; dy = y1-y2; dz = z1-z2
mag = dt * (dx*dx+dy*dy+dz*dz)**(-1.5)
v1[0] -= dx * m2 * mag # ... y, z
v2[0] += dx * m1 * mag # ... y, z
for (r, [vx, vy, vz], m) in bodies:
r[0] += dt * vx # ... y, z
Data: each body = ([x,y,z], [vx,vy,vz], mass), lists updated in place
Libraries: none, plain Python floats (pyperf only for timing)
Notes: nbody is the classic N-body program. Each step computes the gravitational pull for all 10 pairs of bodies, updates velocities, then positions. Positions and velocities are small Python lists that are updated in place. There is no numeric library: every operation is a Python float operation. Keep this code in mind: the lists are the key.

## Slide 5
2
raytrace: a ray tracer in pure Python
100 x 100 image: 7 spheres, a checkerboard floor, 2 lights
camera
sphere
floor
shadow rays to each light
reflection (recursive)
camera ray
Per pixel: closest hit -> colour = reflection + diffuse + ambient
reflection: rayColour calls itself again (up to 4 levels deep)
diffuse: one shadow ray per light, tested against every object
Data: Vector and Point classes (x, y, z) with tiny methods: dot, scale, __sub__, plus no-op type checks (mustBeVector, isPoint)
almost every arithmetic step creates a new Vector object
Libraries: math, array (pixel buffer), pyperf
Notes: raytrace renders a small image. For each pixel it finds the closest object, then computes colour from a reflected ray (recursion), shadow rays to the two lights, and ambient light. The code is very object-oriented: Vector and Point objects with small methods. Remember the shadow rays and the Vector objects: that is where the time goes.

## Slide 6
3
Our profiling toolbox
Flame graphs show WHERE the time goes; counters and the code show WHY
1
perf report
project guide command, python3-dbg
Which CPython C functions run: dispatch, list access, dict lookups, calls
2
Flame graph (pyperformance)
pyperformance --hook perf_record
The same, as a picture; only the timed benchmark code is recorded
3
Flame graph (py-spy)
samples Python's own frames
Python function names and source lines, with the call tree
4
perf stat
hardware counters, fixed work
Instructions, IPC, cache misses, branch misses: memory or compute?
Plus cProfile for call counts, and small timeit/dis experiments to confirm a suspect before changing code. Python 3.10 has no frame pointers, so perf cannot name Python functions: that is why we added py-spy.
Notes: We used four complementary tools. perf report is the command from the project guide; with python3-dbg it names the interpreter's C functions. pyperformance's perf_record hook generates the flame graph the project asks for. Because Python 3.10 has no frame pointers, those flame graphs have no Python names, so we added py-spy, which shows functions and lines. perf stat tells us whether we are memory-bound or not.

## Slide 7
3
nbody: where the time goes
The math is cheap. The interpreter around it is not.
Chart: 
| interpreter loop | float arithmetic | list indexing | float objects | pow (**)
share of time (%) | 44.9 | 19.4 | 14.8 | 12.9 | 1.8
C-level flame graph (pyperformance), self time. Counters: IPC 2.94, cache misses 4.3%, branch misses 0.37%: not memory, not branches.
py-spy: hottest lines of advance()
48.3%
v1[0] -= dx*b2m ... v2[2] += dz*b1m
18.3%
mag = dt * (d2) ** (-1.5)
10.6%
r[0] += dt * vx ...
8.4%
for ((x1,y1,z1),v1,m1), ... in pairs
list read/write lines: ~59% of the run time
Notes: Left: the flame graph from pyperformance, grouped by kind of work. Almost half is the bytecode dispatch loop; list indexing is 15 percent; pow, the one expensive math function, is only 1.8 percent. Right: py-spy shows the same thing per Python line: the six velocity-update lines alone are 48 percent. The counters say it is not a memory problem: the CPU just executes many instructions per float operation.

## Slide 8
3
Why v[0] -= x is expensive
Checked with dis and timeit before changing any code
# local variable: x
LOAD_FAST x
# list element: v[0]
LOAD_FAST v
LOAD_CONST 0
BINARY_SUBSCR # type check, index check
A list element costs extra bytecodes and C calls (type check, index conversion, fetch). nbody does 75 list reads and 75 list writes per step, 20000 steps per call.
Chart: 
| read | update (-=)
local variable | 17 | 38
list element | 33 | 80
timeit on the VM, nanoseconds per operation
Notes: This is the experiment that told us what to do. A local variable is one LOAD_FAST, a slot in the frame. A list element is three bytecodes plus type and bounds checks. Reading is 2 times slower, updating too. One access is only 40 nanoseconds extra, but nbody does 1.2 million list updates per run, so it adds up.

## Slide 9
4
nbody fix: keep the state in local variables
Copy once at the start of advance(), compute on locals, write back once at the end
(r0, v0, m0), ... (r4, v4, m4) = bodies
x0, y0, z0 = r0; vx0, vy0, vz0 = v0 # ...
for _ in range(n):
# pair (0, 1)
dx = x0 - x1; dy = y0 - y1; dz = z0 - z1
mag = dt * ((dx*dx+dy*dy+dz*dz)**(-1.5))
vx0 -= dx * (m1*mag) # locals only
# ... 9 more pairs, then positions
r0[0] = x0; v0[0] = vx0 # write back once
Same operations in the same order, so the output is bit-for-bit identical (verify_nbody.py, 20000 steps). Other body counts fall back to the original loop.
1.60x
faster 230.4 -> 144.3 ms median
-34%
instructions (perf stat, same work)
0%
list indexing left in the flame graph (was 14.8%)
1.65x
second session: reproducible
Notes: The fix follows directly from the profile. We copy positions and velocities into local variables once, run all 20000 steps on locals, and write back once. Because the operations and their order are unchanged, the result is bit-identical. 1.60 times faster, a third fewer instructions, and list indexing disappears from the flame graph. Trade-off: the 10 pairs are written out, so it is specialised to 5 bodies with a fallback for other sizes.

## Slide 10
4
A change that did not help: ** -> sqrt
mag = dt / (d2 * sqrt(d2)) is mathematically the same as dt * d2 ** (-1.5)
1.8%
pow's share of the time: the profile predicted ≤ 2% gain
1.01x
slower when measured (and locals+sqrt slower than locals alone)
n.s.
sqrt as a local variable: 143.3 vs 143.7 ms, not significant
Why: in Python the cost is not the math. d2 ** (-1.5) is one bytecode that calls C pow directly (86 ns); 1/(d2*sqrt(d2)) needs a lookup of sqrt, a call, a multiply and a divide (93 ns).
Decision: dropped, kept **. The measurement stays in the report as a negative result that the profile correctly predicted.
Notes: sqrt is one CPU instruction, so replacing pow looked like a win. The flame graph said otherwise: pow is only 1.8 percent of the time. Measured, it was 1 percent slower, because calling sqrt from Python costs more than pow saves. Even making sqrt a local variable gave no significant difference. Lesson: measure, do not assume.

## Slide 11
3
raytrace: where the time goes
Python-level flame graph (py-spy): width = share of run time
bench_raytrace > render
rayColour
colourAt
listcomp: intersect all
_lightIsVisible (shadow rays)
rayColour (reflect)
Ray() built again
intersect
intersectionTime from all callers: 43% (dot 20%, __sub__ 22%)
C level: function calls 19.8%, dict lookups 17.7%, math 0.1%
cProfile: 3.09 million Python calls and 453k new Vectors per image
Bottlenecks
the same shadow ray rebuilt for every object (~28%)
~7 tiny method calls and a temporary Vector per ray-object test
every Vector/Point has its own attribute dictionary
Notes: This is a simplified copy of the py-spy flame graph. Nearly half the time is in _lightIsVisible, the shadow-ray check, and more than half of that is building the same Ray object again for every object in the scene. intersectionTime is 43 percent, mostly its small helper methods. At C level the picture is calls and dictionary lookups; the math itself is almost free. Unlike nbody, the problem is the object-oriented structure.

## Slide 12
4
raytrace fixes: three targeted changes
Each measured on its own, each renders a bit-identical image
shadow_ray
Build Ray(p, l - p) once per light, not once per object
1.30x
sphere_floats
intersectionTime with plain floats: no temporary Vector, no dot/__sub__ calls
1.34x
slots
__slots__ = ('x','y','z'): no per-object dictionary
1.12x
combined
2.10x
Chart: 
| original | shadow_ray | sphere_floats | slots | combined
median (ms) | 807 | 620.7 | 601.1 | 719.1 | 385
Savings overlap: 186 + 206 + 88 ms separately, but combined 385 ms, not 327 (fewer shadow rays also means fewer Vectors to speed up).
Notes: Three changes, each aimed at one bottleneck from the flame graph. Build the shadow ray once: 1.30x. Compute the sphere intersection with plain floats: 1.34x. __slots__ removes the per-object dictionary: 1.12x. Together 2.10x. They do not simply add up, because they overlap: once fewer rays are built, there are fewer Vectors for slots to speed up.

## Slide 13
4
Software results
pyperformance --rigorous, 120 samples each, same tuned session
Chart: 
| nbody | raytrace
original | 230.4 | 807
optimized | 144.3 | 385
1.60x
nbody 37% less time
2.10x
raytrace 52% less time
-34%
nbody instructions
-52%
raytrace instructions
Target: 7% on two benchmarks. Both outputs bit-identical.
Notes: Summary of the software part. Both benchmarks are far above the 7 percent target, and both produce exactly the same output as before. The counters show why: we execute a third fewer instructions in nbody and half in raytrace. Cache and branch behaviour barely changed, which confirms the bottleneck was interpreter work, not memory.

## Slide 14
5
Why a hardware accelerator, and why nbody
What is left after the software fix cannot be removed in Python
~100%
of nbody's time is one loop, advance(): Amdahl is on our side
51%
of the optimized code is float arithmetic + float objects: only hardware removes that
280 B
of state (5 bodies x 7 doubles): one transfer in, one out per call
raytrace instead? its math is only ~6% of the time; the cost is Python calls and objects. A ray-sphere unit would speed up that 6% and leave the rest in Python.
nbody: the whole advance() loop moves to hardware; 20000 steps run with no software in between.
Notes: Why nbody: the whole benchmark is one loop, so offloading it leaves almost nothing on the CPU. After our software fix, half of what remains is float arithmetic and float objects, which no Python rewrite can remove. And the state is tiny, so PCIe is used once per call. raytrace's math is only 6 percent of its time, so accelerating it would not pay.

## Slide 15
5
The accelerator in the system
FPGA card on PCIe, 100 MHz, IEEE-754 double precision like Python
HOST (CPU)
Python benchmark
advance(dt, n) - unchanged
nbody_accel_driver.py
card? write regs, START, wait, read back. No card: software
OS: PCIe driver
mmap BAR0, IOMMU, interrupt
PCIe
ACCELERATOR CARD (FPGA)
PCIe endpoint
MMIO: addr 16, data 64
Registers
CTRL, STATUS, N, STEPS, DT, CYCLES + body state (16)
Controller FSM
FEED > DRAIN > ACC > POS > next step
Pair force pipeline
81 cycles, 1 new pair per cycle
Accumulator + position update
6 adders (pair order) · 3 mul + 3 add
irq_done -> host when all steps are done
Notes: The host side: the benchmark calls advance exactly as before; the driver writes the bodies and parameters into the card's registers over PCIe, starts it, waits for the done interrupt or polls STATUS, and reads the result back. If there is no card it runs the normal software, so nothing breaks. On the card: registers and body state, a controller FSM, the pair force pipeline, and the accumulator and position update.

## Slide 16
5
Inside: pair force pipeline and control
Pairs are independent within a step (forces depend only on positions)
S1
dx,dy,dz
3 add
3 cycles
S2
squares
3 mul
4 cycles
S3-4
d2 = sum
2 add
6 cycles
S5
sqrt(d2)
sqrt
28 cycles
S6
d2 * r
mul
4 cycles
S7
dt / den
div
28 cycles
S8
m * mag
2 mul
4 cycles
S9
6 deltas
6 mul
4 cycles
81 cycles latency · div and sqrt: digit recurrence, 2 bits per stage, 28 stages each · all IEEE-754 double, round to nearest even
IDLE
wait for START
FEED
one pair per cycle into the pipeline
DRAIN
wait for the last result
ACC
apply deltas in pair order
POS
update positions body by body
STEP_END
next step or DONE + irq
Measured cycles per step = 6P + 11N + 84 benchmark (N = 5, P = 10): 199 cycles = 1.99 µs at 100 MHz
Notes: The pipeline mirrors the software formula stage by stage. A new pair can enter every cycle, and results come out 81 cycles later; sqrt and divide are the long stages. The accumulation must follow pair order to be bit-exact, because float addition is not associative. The cycle formula was measured in simulation for 2, 3, 5 and 16 bodies and fits exactly: 84 is the pipeline plus control, 6 per pair, 11 per body.

## Slide 17
5
How software talks to it
Memory-mapped registers in PCIe BAR0, 64-bit so one register holds one double
offset | register | meaning
0x0000 | ID | "NBODYACC": driver detects the card
0x0008 | CTRL | bit0 START
0x0010 | STATUS | BUSY, DONE
0x0018 | NUM_BODIES | 2 .. 16
0x0020 | NUM_STEPS | steps per call
0x0028 | DT | IEEE-754 double
0x0030/38 | STEPS_DONE, CYCLES | progress, performance counter
0x1000+ | BODY[b].f | x y z vx vy vz m
advance = accelerated(advance)
advance(0.01, 20000) # same call
card present: write N, steps, dt, 35 body values; START; wait for DONE; read back into the same lists
70 register operations per call, independent of the number of steps
no card, or > 16 bodies: the normal software advance() runs
large systems: one DMA transfer instead of register writes
Notes: The whole interface is this register map. The driver wraps the benchmark's own advance function, so the benchmark code does not change: that follows the rule from the accelerator lecture, keep changes inside a library and never break user code. Seventy register operations per call, no matter how many steps.

## Slide 18
5
Verification: bit for bit
Icarus Verilog simulation, run_tests.sh rebuilds and reruns everything
274,014
floating-point test vectors: add, mul, div, sqrt vs Python's IEEE-754 results, 0 errors
4 / 4
system tests through the registers: real benchmark bodies and 2, 3, 16 bodies, bit-identical
20,000
steps of the real benchmark call: 3,980,000 cycles, all 35 values bit-identical
2 / 2
driver paths: software fallback and offload, both identical
Same results as the software: IEEE double with 1/(d2·sqrt(d2)), because +, -, x, / and sqrt have exactly one correct IEEE result and pow does not. Bit-identical to the software with the same formula; vs the original **: 1.3e-9 relative after 20000 steps (rounding only).
Notes: We checked the hardware at three levels. Each floating-point unit against Python, bit for bit, on 274 thousand vectors including cancellation and rounding ties. The whole accelerator, driven only through its registers like the driver would, against the real benchmark code, including a full 20000-step call. And the driver in both modes. The only difference from the original is sqrt instead of pow: same math, rounding-level difference.

## Slide 19
5
Estimated speedup (from measured numbers)
Software: pyperformance medians. Hardware: simulated cycles x 10 ns + PCIe overhead
Chart: 
| original SW | optimized SW | accelerator
ms per iteration | 232.2 | 143.7 | 41
accelerator = 20000 x 199 cycles x 10 ns (39.8 ms) + 70 PCIe accesses at 10 µs + polling (1.2 ms)
5.7x
vs original software
3.5x
vs our optimized software
Break-even: the PCIe cost is paid once per call, so the card wins above ~125 steps (vs original) or ~230 (vs optimized). The benchmark does 20000.
More bodies, bigger win: 1.3x at 2, 3.6x at 5, 5.1x at 8, 6.6x at 16 bodies.
Assumptions: 100 MHz reached (not synthesized), 10 µs per register access (pessimistic), FPGA configured once.
Notes: The estimate uses only measured numbers: the software times from pyperformance and the cycle count from simulation. 41 milliseconds per iteration instead of 232: 5.7 times faster than the original, 3.5 times faster than our optimized Python. The overhead is paid per call, not per step, so the card only pays off with many steps per call.

## Slide 20
5
Design trade-offs
Performance, area, frequency and power
IEEE double vs fixed point
Exact same results as the software. Fixed point is smaller and uses less power, but drifts over 20000 steps.
Div/sqrt: bits per stage
2 bits at 100 MHz is our balance. 1 bit: ~150 MHz, 2x registers, more power. 4 bits: smaller, but ~50 MHz.
Accumulation order
Must follow pair order to stay exact: float addition is not associative.
Parallelism vs area
Parallel position update: -20% cycles for 5x that area. A second pipeline: latency, not throughput, is the limit.
MMIO vs DMA
Registers for small systems (70 accesses). DMA of one buffer for large systems, with IOMMU setup.
Power and energy
CPU busy 232 ms vs card done in 41 ms: energy per run drops, if the FPGA is configured once and stays ready.
Notes: Our trade-off analysis. Be ready to defend each one: why double and not fixed point (exactness), why 2 bits per stage (balance of clock, registers and power), why the accumulation is sequential (associativity), why not more parallel hardware (latency dominates), MMIO versus DMA, and the energy argument with its assumption.

## Slide 21
Conclusions
1
Measure before you trust
Tuned VM, 120 samples, medians: the noise was bigger than the target at first.
2
Python's cost is the interpreter
Not the math: list access, calls, objects, dictionaries.
3
Profile, then change one thing
Every fix came from a flame graph, and the profile even predicted the one that failed.
4
Offload the whole loop
Hardware wins on big batches: 20000 steps per PCIe round trip.
1.60x / 2.10x
software: nbody / raytrace, identical outputs
5.7x
nbody accelerator (estimate), verified bit for bit in simulation
Thank you. Questions?
Notes: Four take-aways. Close with the numbers and invite questions.

## Slide 22
Demo: everything is reproducible
All in the Git repository
# software: setup, verify, profile, benchmark, compare
sudo ./script_nbody.sh
sudo ./script_raytrace.sh
sudo SKIP_SETUP=1 FAST=1 ./script_nbody.sh # quick
# correctness only
python3 nbody/verify_nbody.py
python3 raytrace/verify_raytrace.py
# hardware: FP units, accelerator, driver
hw/nbody_accel/run_tests.sh
python3 hw/nbody_accel/model/estimate_speedup.py
Reports: report_nbody.txt, report_raytrace.txt
Flame graphs: results/profiling/<bench>/<version>/
Raw timings: results/*.json + commands
Hardware: hw/nbody_accel/ (docs, rtl, tb, sw)
AI prompts: prompt.txt
Notes: Backup slide for the live demo. Good quick demos: verify_nbody.py (seconds), run_tests.sh (about 3 minutes, shows the bit-exact hardware tests and cycle counts), and opening a py-spy flame graph SVG in the browser.